Baxi S.p.A.
                                                                      36061 Bassano del Grappa (VI)
                                                                       Italy
                                                                      Via Trozzetti, 20
                                                                       Tel: +39 0424 517111

code 8510910 -  CABLE-GAS VALVE/IGNITER

Characteristics : Electric component

When Igniter receives input voltage (~220V) It creates high voltage impulses which produce sparks on ignition electrode to fire gas on the burner.

Technical Characteristics :

Nominal tension : 220-240Vac - 50/60Hz +10% -15%

Range temperature : -20 °C +100 °C

Nominal frequency of discharges : 10 Hz ± 30%

Material : Cover in PA6 + 30% glass fiber color dark brown

### Weight :  0,124 Kg  (net 0,116 Kg)