Baxi S.p.A.
                                                                      36061 Bassano del Grappa (VI)
                                                                       Italy
                                                                      Via Trozzetti, 20
                                                                       Tel: +39 0424 517111

code 8419060 –    IGNITION UNIT - NAC

Characteristics : Electric component

When Igniter receives input voltage (~220V) It creates high voltage impulses which produce sparks on ignition electrode to fire gas on the burner.

Technical Characteristics :

Nominal tension : 230Vac – 50Hz

Range temperature : -20 °C +100 °C

Nominal frequency of discharges : 4Hz ±  9Hz to 230Vac

Material : Cover in PA6 + 25% glass fiber color red + electric cable + plastic

### Weight :  0,111 Kg  (net 0,102 Kg)